## Slide 1: A Case Against Small Data Types in GPGPUs
Ahmad Lashgar and Amirali Baniasadi
ECE Department
University of Victoria

## Slide 2: Evaluation of Datatype Size on GPGPUs
Key Observation:
  Smallest datatypes always improve memory efficiency
  But they may degrade performance
Key Question:
  Why smaller data type may degrade performance?
Key Finding:
  Miss Status Holding Registers (MSHRs) are the contenting resource under smaller data types

## Slide 3: Outline
Motivation
Background
  GPU Architecture
  Miss status handling structure
Case Study: 1D Stencil
  Memory pattern
  Methodology
  Evaluation

## Slide 4: Impact of Data type Size
Performance vs Accuracy:
  We relax accuracy constrain and evaluate performance
Datatype sizes:
  4-byte int, 2-byte short, 1-byte char
Basic elements of applications:
  Matrix multiplication: Element in matrix
  1D stencil: Element in array
  Stereo matching: Label in disparity map
Case Study

## Slide 5: GPU Architecture
Intercon. Network
L2$
SM
L1$
L2$
MCtrl
MCtrl
SM
L1$
SM
Warp Pool
Warp Scheduler
ALU
SFU
LSU
L1$
Data
Tags
MSHRs
Registerfile
MSHRs
W0
-
MW0
W1
-
MW1
L0
-
$ID
0x0A
-
ADDR
-
-
-
-
-
-
-
-
Merger fields
Cache line
Block address

## Slide 6: Outstanding memory accesses
Limited by L1$ and MSHRs capability
Without merging capability:
Best-case merging-enabled:
Worst-case merging-enabled:
Notes: #MSHR -> number of MSHR entries
#MSHRMergers -> number of merger fields per MSHR entry
#cacheLines -> number of cache line in L1 cache
#wayInaSet -> number of sets in a L1 cache

## Slide 7: Case Study: 1D Stencil
Algorithm:
CUDA code:
int i = threadIdx.x + blockIdx.x*blockDim.x;
if( i<(n-1) && i>0 ){
a_dst[i] = (a_src[i-1] + a_src[i] + a_src[i+1]) / 3;
}
Notes: We investigate 1D stencil, under real and simulated hardware, to understand why smaller data types may degrade performance

## Slide 8: Methodology
Real hardware:
  NVIDIA GeForce GTX480
Simulated hardware:
  GPGPU-sim v3.2.2
  GTX480
  32-MSHR per L1$, 8-merger per MSHR entry

## Slide 9: Performance
Stencil 1D under real and simulated GTX480

## Slide 10: Memory efficiency
Smaller data types consistently improve memory efficiency metrics:

## Slide 11: Stall breakdown
Smaller datatypes stall for merger fields
Larger datatypes stall for coalescing

## Slide 12: Conclusion
Real evaluation and simulation to observe the impact of datatypes on:
  Performance of GPUs
  Effective cache capacity, memory latency/bandwidth/demand
  Coalescing, cache, and MSHR stalls
Smaller datatypes improve memory efficiency
Depending on the memory access pattern, smaller datatypes may increase MSHR merger stalls
Future Work:
  Micro-benchmarking to understand GPU MSHR structure

## Slide 13
Thank you!
Question?

## Slide 14: Example: Worst-case scenario
Warp Pool
Warp Scheduler
L1$
Data
Tags
MSHRs
X
X
X
X
W0
-
MW0
W1
-
MW1
L0
-
$ID
0x0A
-
ADDR
ALU
SFU
LSU
Registerfile
L0
L1
L0
L1
W2
0x0A
W0
ALU
W1
ALU
W2
ALU
W3
LSU
W4
LSU
W5
LSU
W6
LSU
W7
LSU

## Slide 15: Methodology (2)

## Slide 16: Methodology (3)

## Slide 17: Sensitivity
Varying MSHRs, merger fields, sets, and ways