## Slide 1: Understanding Outstanding Memory Request Handling Resources in GPGPUs
Ahmad Lashgar, Ebad Salehi, and Amirali Baniasadi
ECE Department
University of Victoria
June 1, 2015
The Sixth International Symposium on Highly Efficient Accelerators and Reconfigurable Technologies (HEART 2015)

## Slide 2: This Work
GPUs are energy-efficient high-throughput processors
Understanding GPUs is critical
We discover GPU microarchitecture details
HOW? We develop resource targeting microbenchmarks.
GPU
Memory pressure
Delay Analysis

## Slide 3: Outline
Overview
GPU Micro-architecture design
Outstanding Memory Access Handling Unit
  MSHR or PRT
Thread-Latency plot
Micro-benchmarking Fermi and Kepler GPUs
Conclusions
Notes: -Alternative designs for handling outstanding memory accesses

## Slide 4: NVIDIA-like GPU Micro-architecture
Each SM is a multi-threaded SIMD core
GPU
DRAM
SM1
SMN
…
MC1
MCN
L1$
L1$
L2$
L2$
Interconnect
…
SMN
L1$
Warp Pool
Warp 1 | PC | T1 T2 T3 T4 |
Warp 2 | PC | T5 T6 T7 T8 |
Load/Store Unit
Int/Float
Unit
Special Fcn
Unit
…
Tag
Data
Outstanding mem. access handling unit
Outstanding memory access handling unit
?
Scoreboard

## Slide 5: Outstanding Memory Access Handling Unit
MSHR
  Miss Status/Information Holding Register
  Used in GPGPU-sim [Bakhoda’2010]
PRT
  Pending Request Table
  Introduced in an NVIDIA patent [Nyland2013]

## Slide 6: MSHR
First structure known as memory access handling unit:
  Miss Status/Information Holding Register
A table of N entries
Each entry tracks one missing memory block
Each entry can be shared among M memory requests

## Slide 7: MSHR Sample Operation
Issued Instruction
To the Lower Memory Level
From the Lower Memory Level
Tag
MSHR
#1 |  |  |  | 
#2 |  |  |  | 
#3 |  |  |  | 
#4 |  |  |  | 
N entry
M merged threads
Block addr.
T1
Warp 1 | PC | T1 T2 T3 T4 |
Load/Store Unit
T1 | T2 | T3 | T4
0x0A40 | 0x0A44 | 0x0A50 | 0x0A54
T2
T5 | T6 | - | T8
0x0A64 | 0x0A68 | - | 0x0A6F
Warp 2 | PC | T5 T6 - T8 |
0x0A4 | #1
0x0A4
0x0
0x04
0x0A5 | #2
MSHR ID
MSHR ID
Block addr
0x0A6 | #3
T3
T4
0x0A5
0x0
0x04
SM
L1 $
Data
DATA | #1
DATA | #2
DATA | #3
Cache Miss
T5
T8
T6
0x0A6
0x04
0x0F
0x08

## Slide 8: PRT
Second structure known as memory access handling unit:
  Pending Request Table
A table of N entries
Each entry tracks one warp memory instruction
Each entry may generate multiple memory requests
  Thread mask specifies the associated threads

## Slide 9: PRT Sample Operation
Issued Instruction
To the Lower Memory Level
From the Lower Memory Level
Tag
PRT
#1 |  |  |  |  |  | 
#2 |  |  |  |  |  | 
#3 |  |  |  |  |  | 
#4 |  |  |  |  |  | 
N entry
Offsets in mem. blocks
Warp ID
2
T1
T3
T4
Warp 1 | PC | T1 T2 T3 T4 |
Load/Store Unit
T1 | T2 | T3 | T4
0x0A40 | 0x0A44 | 0x0A50 | 0x0A54
T2
T5 | T6 | - | T8
0x0A64 | 0x0A68 | - | 0x0A6F
Warp 2 | PC | T5 T6 - T8 |
0x0A4 | #1 | 1100
Warp1
Pending Requests
0x0
0x0
0x04
0x04
0x0A5 | #1 | 0011
PRT ID
PRT ID
Block addr
Thread mask
0x0A6 | #2 | 1101
1
T5
T7
T8
T6
Warp2
0x04
-
0x0F
0x08
SM
L1 $
Data
1
DATA | #1 | 1100
DATA | #1 | 0011
DATA | #2 | 1101
Cache Miss
Warp size

## Slide 10: Stressing Memory Access Handling Unit
Single-thread multiple-loads
tic = clock();
char Ld1 = A[128*1];
char Ld2 = A[128*2];
char LdN = A[128*N];
toc = clock();
Time = toc – tic;
....
kernel<<<1,1>>>(...)
Multiple-loads (N)
Time
1
2
3
4
5
6
7
8
Which resource is
saturated?
Scoreboard 

## Slide 11: Stressing Memory Access Handling Unit (2)
Parallel-threads single-load
tic = clock();
char Ld1 = A[128*1];
__syncthreads();
toc = clock();
Time = toc – tic;
....
kernel<<<1,M>>>(...)
Parallel-threads (M)
Time
8
16
32
48
64
80
96
Which resource is
saturated?
Outstanding memory
access handling unit

## Slide 12: Stressing Memory Access Handling Unit (3)
Parallel-threads multiple-loads
tic = clock();
char Ld1 = A[128*1];
char Ld2 = A[128*2];
char LdN = A[128*N];
__syncthreads();
toc = clock();
Time = toc – tic;
....
kernel<<<1,M>>>(...)
Parallel-threads (M)
Time
8
16
32
48
64
80
96
1 load
2 load
4 load
Found a way to occupy resources:
Parallel-threads multiple-loads

## Slide 13: MSHR vs PRT test?
Parallel-threads single-load
  Different memory patterns:
All Unique:
Every thread fetches a
unique memory block
Parallel-threads
Time
X
MSHR respond:
Two-Coalesced:
Every two neighbor
threads fetch a common
unique memory block
Parallel-threads
Time
Y
PRT respond:
Parallel-threads
Time
X
MSHR respond:
Parallel-threads
Time
Y
PRT respond:
2X
Notes: -How to understand if the structure is MSHR or PRT?

## Slide 14: Finding MSHR Parameters
Memory patterns:
  All Unique
  Two-coalesced
  Four-coalesced
  Eight-coalesced
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | 
128-byte blocks
Global Memory address space
#10
#9
#8
#7
#6
#5
#4
#3
#2
#1
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #2 | #2 | #3 | #3 | #4 | #4 | #5 | 
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #1 | #1 | #2 | #2 | #2 | #2 | #3 | 
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #1 | #1 | #1 | #1 | #1 | #1 | #2 | 

## Slide 15: Thread-Latency Plot
Loads/thread: 1, pattern: All Unique
Notes: -spikes in variance of latency shows huge change in latency.
-lack of data around the beginning of X, e.g. 0 thread, leads to distortion.
-we found three neighbors large enough to find the spike and small enough to avoid smoothing effects.

## Slide 16: Methodology
Two NVIDIA GPUs:
  Tesla C2070 (Fermi architecture)
  Tesla K20c (Kepler architecture)
CUDA Toolkit v5.5
Micro-benchmarking the GPU:
  MSHR or PRT?
  Find the parameters of MSHR or PRT structure

## Slide 17: #1 Fermi: MSHR vs PRT Test?
Multiple-threads single-load
Memory Pattern:
All Unique:
Every thread fetches a
unique memory block
Two-Coalesced:
Every two neighbor
threads fetch a common
unique memory block
May not be PRT
MSHR

## Slide 18: #1 Fermi: MSHR Parameters
Loads per thread (LdpT)
Pattern (1=All Unique, 2=Two-coalesced, etc)
Threads
# warp = Threads / 32
Unique mem = LdpT * (Threads / Pattern)
max # MSHR entries = Unique mem
min # MSHR mergers = pattern
1
1
128
4
128
128
1
Loads/thread: 1, pattern: All Unique
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | 
Loads/thread: 1, pattern: Two-Coalesced
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #2 | #2 | #3 | #3 | #4 | #4 | #5 | 
1
2
256
8
128
128
2
Loads/thread: 2, pattern: Four-Coalesced
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #1 | #1 | #2 | #2 | #2 | #2 | #3 | 
 | #a | #a | #a | #a | #b | #b | #b | #b | #c | 
2
4
256
8
128
128
4
Loads/thread: 4, pattern: Eight-Coalesced
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #1 | #1 | #1 | #1 | #1 | #1 | #2 | 
 | #a | #a | #a | #a | #a | #a | #a | #a | #b | 
 | #^ | #^ | #^ | #^ | #^ | #^ | #^ | #^ | #$ | 
 | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᶋ | 
4
8
256
8
128
128
8
We didn’t observe spike beyond merger8
Conclusion: 128 entries + 8 mergers per entry at least
Config
Spike
Finding

## Slide 19: #2 Kepler: MSHR vs PRT Test?
May not be MSHR
PRT
Multiple-threads two-loads
Memory Pattern:
All Unique:
Every thread fetches a
unique memory block
Two-Coalesced:
Every two neighbor
threads fetch a common
unique memory block

## Slide 20: #2 Kepler: PRT Parameters
Loads per thread (LdpT)
Pattern (1=All Unique, 2=Two-coalesced, etc)
Threads
# warp = Threads / 32
Unique mem = LdpT * (Threads / Pattern)
max # PRT entries = # warp x LdpT
2
1
678
~22
1356
~44
3
1
454
~15
1362
~45
1
1
NoSpike
-
-
-
We observed scoreboard saturation beyond 3LdpT
Conclusion: 44 entries at least

## Slide 21: Conclusion
Findings:
  Tesla C2070: MSHR
    128 MSHR entry, utmost, 8 mergers per entry, at least
    MLP per SM:
      Coalesced = 1024 (128 x 8)
      Un-coalesced = 128
  Tesla K20c: PRT
    44 PRT entries, utmost, 32 requests per entry (warp size)
    MLP per SM:
      Coalesced/Un-coalesced = 1408 (44 x 32)
Optimization for programmer
  Diminishing return of coalescing on recent architectures
Notes: -We observe slight sensitivity to coalescing under K20c, which shows it’s a powerful architecture in MLP. e.g. we compared naiive matrix-matrix multiplication to tiling optimized version under both architectures.

## Slide 22
Thank You!
Questions?

## Slide 23: References
[Nyland2013] L. Nyland et al. Systems and methods for coalescing memory accesses of parallel threads, Mar. 5 2013. US Patent 8,392,669.
[Bakhoda’2009] A. Bakhoda et al. Analyzing cuda workloads using a detailed gpu simulator. In ISPASS 2009.

## Slide 24: Micro-benchmark Skeleton
Modifying the UNQ procedure to get different memory patterns
  Each access is unique
  Every two, four, eight, 16, or
  32 neighbor threads access a
  unique block
nThreads:
  1 - 1024
Notes: -Simplify this slide.

## Slide 25: Thread-Latency Plot
Loads/thread: 1, pattern: merger1
Notes: -spikes in variance of latency shows huge change in latency.
-lack of data around the beginning of the of X, e.g. 0 thread, leads to distortion.
-we found three neighbors large enough to find the spike and small enough to avoid smoothing effects.

## Slide 26: #1 Tesla C2070: MSHR or PRT Test?
Loads per thread (LdpT)
Pattern (merger1, 2, 4, 8)
Threads
# warp = Threads / 32
Unique mem = LdpT * (Threads / Pattern)
max # PRT entries = # warp x LdpT
max # MSHR entries = Unique mem
Loads/thread: 1, pattern: merger1
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | 
1
1
128
4
128
4
128
2
1
64
2
128
4
128
1
2
256
8
128
8
128
Loads/thread: 2, pattern: merger1
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | 
 | #a | #b | #c | #d | #e | #f | #g | #h | #i | 
Loads/thread: 1, pattern: merger2
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #2 | #2 | #3 | #3 | #4 | #4 | #5 | 
May not be PRT
MSHR

## Slide 27: #1 Tesla C2070: MSHR Parameters
Loads per thread (LdpT)
Pattern (merger1, 2, 4, 8)
Threads
# warp = Threads / 32
Unique mem = LdpT * (Threads / Pattern)
max # MSHR entries = Unique mem
min # MSHR mergers = pattern
1
1
128
4
128
128
1
Loads/thread: 1, pattern: merger1
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | 
Loads/thread: 1, pattern: merger2
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #2 | #2 | #3 | #3 | #4 | #4 | #5 | 
1
2
256
8
128
128
2
Loads/thread: 2, pattern: merger4
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #1 | #1 | #2 | #2 | #2 | #2 | #3 | 
 | #a | #a | #a | #a | #b | #b | #b | #b | #c | 
2
4
256
8
128
128
4
Loads/thread: 4, pattern: merger8
thread block | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | …
 | #1 | #1 | #1 | #1 | #1 | #1 | #1 | #1 | #2 | 
 | #a | #a | #a | #a | #a | #a | #a | #a | #b | 
 | #^ | #^ | #^ | #^ | #^ | #^ | #^ | #^ | #$ | 
 | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᵷ | #ᶋ | 
4
8
256
8
128
128
8
We didn’t observe spike beyond merger8
Conclusion: 128 entries + 8 mergers per entry at least

## Slide 28: #2 Tesla K20c: MSHR or PRT Test?
Loads per thread (LdpT)
Pattern (merger1, 2, 4, 8)
Threads
# warp = Threads / 32
Unique mem = LdpT * (Threads / Pattern)
max # PRT entries = # warp x LdpT
max # MSHR entries = Unique mem
2
1
678
~22
1356
44
1356
2
2
682
~22
682
44
682
2
4
682
~22
341
44
341
May not be MSHR
PRT
Notes: -remove third column

## Slide 29: #2 Tesla K20c: PRT Parameters
Loads per thread (LdpT)
Pattern (merger1, 2, 4, 8)
Threads
# warp = Threads / 32
Unique mem = LdpT * (Threads / Pattern)
max # PRT entries = # warp x LdpT
2
1
678
~22
1356
~44
3
1
454
~15
1362
~45
1
1
NoSpike
-
-
-
We observed scoreboard saturation beyond 3LdpT
Conclusion: 44 entries at least

## Slide 30: Stressing Outstanding Memory Access Resources
Thread Block
Launch single thread block
  1 to 1024 threads
Each threads fetches single unique memory block
Multiple loads per thread
  1 to 4 loads
128-byte blocks
Global Memory address space
0x0000
0x0080
0x0100
0x0180
0x0200
0x0280
Thread#3
Thread#2
Address
Address
Address
Address
Thread#1
Address
Address
First Load
Second load
Notes: -To occupy outstanding memory accessing resources on single SM
-Stop before saturating the scoreboard