## Slide 1: Rethinking Prefetching in GPGPUs: Exploiting Unique Opportunities
Ahmad Lashgar and Amirali Baniasadi
ECE Department
University of Victoria

## Slide 2: Overview
Prefetching Challenges:
  Prefetching accuracy
  Timeliness
  Bandwidth control
Proposed scheme:
  Predict data statically in software
  Prefetch dynamically in hardware (per block)
Addressing Challenges in GPGPUs:
  Prefetching accuracy:
    Software: Static analysis
  Timeliness & Bandwidth control:
    Hardware: Stall blocks until prefetching completes
Notes: Put #

## Slide 3: Outline
Static Predictability of Memory Accesses
Proposed Prefetching Scheme
  Software
  Hardware
Experimental Results:
  Machine Models
  Prefetch Buffer Implementation
Notes:   -Share of Predictable & Unpredictable array indexes.

## Slide 4: Static Predictability of Memory Accesses
Steps:
  Parse the kernel
  Extracts all array indexes (global memory accesses)
  Groups indexes based on the predictability of the index
Based on the operators and terms forming the index
  Statically Predictable
  Quasi-static Predictable
  Unpredictable (induction, indirect, control)
__global__ void
kernel(float *outArr, float*inArr){
  int bIdx = blockIdx.x;
  int tIdx = threadIdx.x;
  outArr[bIdx*blockDim.x+tIdx] = inArr[bIdx*blockDim.x+tIdx];
}

## Slide 5: Unpredictable indexes
Index is formed by operators other than + and x
Index depends on runtime terms
  Induction: loop iterator variable
  Indirect: load from another memory location
  Control: a control statement defines the value
e.g. value = array[ 127 / varA + varB ]
e.g. for(int i=0; i<N; i+=m)
value = array[ threadIdx.x + i ]
e.g. value = array[ arrayB[ threadIdx.x ] ]
e.g. value = array[ control ? threadIdx.x : 0 ]

## Slide 6: Predictable
Statically Predictable
  Index is formed by + and x operators and constant terms
Quasi-static Predictable
  Index is formed by + and x operators, constant terms, and CUDA built-in variables
e.g. value = array[ 128*4+5 ]
e.g. value = array[ threadIdx.x ]
e.g. value = array[ blockIdx.x*blockDim.x + threadIdx.x ]
e.g. value = array[ blockIdx.x*13 + threadIdx.x + 9*54 ]

## Slide 7: Predictability Analysis for 14 Benchmarks
Number of arrays and indexes

## Slide 8: Predictability Analysis for 14 Benchmarks (2)
Breakdown of predictability of indexes
Indexes are highly predictable
Key Idea: Pass information about predictable indexes to hardware and
based on runtime value of CUDA built-in variables do prefetching.

## Slide 9: Proposed Prefetching Scheme
Software Side
  Static analyzer to extract information
  Forming information into API calls
  Injecting the calls in the code, immediately before kernel launch
  API calls set a prefetching table in the hardware
Hardware Side
  Prefetch controller
  Prefetch buffer
  Prefetch table

## Slide 10: Simplify the information in form of API
We look for minimum and maximum values that index may have
CUDA built-in variables:
  threadIdx -> Range of this variable is constant
  gridDim and blockDim -> Constant for each kernel
  blockIdx -> Constant for each thread block
Predictable index can be simplified to one CUDA built-in variable
  Example
  If kernel launch sets blockDim.x to 256, then:
value = array[ blockIdx.x*blockDim.x + threadIdx.x ]
Index minimum = blockIdx.x*256 + 0
Index maximum = blockIdx.x*256 + 255

## Slide 11: Proposed API call
Prototype of the API call passing a prefetch stride to hardware
Sets a row in prefetch table on the GPU

## Slide 12: Hardware – Prefetch Table
Every row stores information from one API call and corresponds to an stride of data
Thread Block Dispatch
Prefetch Table
GPU Core #0
Interconn. Network
GPU Core #1
Memory Controller #1
Memory Controller #0
ptr | Type size | min-bxp | min-byp | min-bzp | min-off | max-bxp | max-byp | max-bzp | max-off

## Slide 13: Hardware – Prefetch Controller Unit
Thread Block Dispatch
Prefetch Controller Unit
Prefetch Table
GPU Core #0
Interconn. Network
GPU Core #1
Memory Controller #1
Memory Controller #0
Prefetch controller unit calculates the range of prefetch stride for about-to-dispatch thread blocks from prefetch table:

## Slide 14: Hardware – Prefetch Buffer
Prefetch buffer is a logical buffer at each GPU core to store prefetched data
  can be a dedicated buffer, space from the cache, or shared memory.
Thread Block Dispatch
Prefetch Controller Unit
Prefetch Table
GPU Core #0
Prefetch Buffer
Interconn. Network
GPU Core #1
Prefetch Buffer
Memory Controller #1
Memory Controller #0

## Slide 15: Prefetch Timeliness
Performing prefetching at the thread block granularity
Assuring timeliness:
  Thread block remains inactive on the GPU core until prefetching completes
Stalling the thread block also prevents threads from issuing redundant accesses

## Slide 16: Case Study: BFS
The kernel

## Slide 17: Case Study: BFS
Predictability of array accesses

## Slide 18: Case Study: BFS
API calls

## Slide 19: Methodology
Prefetching scheme is implemented in GPGPU-sim
Benchmarks from RODINIA, CUDA SDK, and Third-Party

## Slide 20: Machine Models
Measure the potential behind the prefetching scheme relaxing the performance overheads
  I-Machine -> No Prefetching Request No thread block stall
  S-Machine-> Prefetching Requests No thread block stall
  R-Machine-> Prefetching Requests Thread block stall
All machines have ideal prefetch buffer (unlimited size, fully-associative)

## Slide 21: Machine Models – Performance
Numbers are normalized to no-prefetching baseline
Labels below the bars show the achievable speedup via ideal zero-latency memory
Notes: -Issuing prefetching request impose significant performance overhead (Comparing I-Machine to S-Machine)
-Overhead of stalling thread block is significant when the total load of block is low (e.g. NNC)

## Slide 22: Machine Models – DRAM Row Locality
Row locality = total accesses / row changes
Numbers above the bars reports R-Machine DRAM accesses, normalized to baseline
Notes: -Generally improves row locality while keeping the total accesses the same (except BPT and EDS)

## Slide 23: Machine Models – Prefetch Buffer
Coverage: percentage of memory accesses that found in prefetch buffer
Buffer size: maximum size of prefetch buffer for a thread block
Notes: As we pointed it out earlier, machine models have unlimited prefetch buffer size.

## Slide 24: Real Implementations - Performance
Implementing the prefetch buffer using a set-associative cache

## Slide 25: Real Implementations - Tuning Prefetching
Potential behind compiler heuristics injecting API calls intelligently
Notes: -Adjusting the prefetching size to the cache size

## Slide 26: Conclusion
Proposed an scheme to statically predict & dynamically prefetch for thread blocks
Evaluations show a clear advantage behind the prefetching scheme
  20% to 49% over the baseline without prefetching
Future work:
  Improving the static analyzer to capture induction unpredictable indexes
  Developing compiler heuristics to adjust API to cache size