## Slide 1: Addressing Software-Managed Cache Development Effort in GPGPUs
Ahmad Lashgar
PhD Candidate at ECE Department
Supervisors:
Dr. A. Baniasadi
Dr. N. J. Dimopoulos
August 8, 2017
PhD Defense Session

## Slide 2: Heterogeneous Computing
Use of different kinds of processing cores for higher efficiency
  From high-performance to low-power embedded systems
High-performance computing style
  Serial workloads run on multiple out-of-order fast cores
    Traditional CPUs
  Parallel workloads run on many in-order slow cores
    Accelerators: GPUs, FPGAs, XeonPhi, etc.

## Slide 3: Accelerator Hardware/Software Stack
Scope of this work: OpenACC-over-CUDA for NVIDIA GPUs

## Slide 4: Hardware
NVIDIA-like GPGPU Microarchitecture
GPU
DRAM
Core1
CoreN
…
MC1
MCM
L1$
L1$
L2$
L2$
Interconnect
…
SMN
L1 Cache
Ready Thread Blocks
Load/Store Unit
Arith/Logic
SIMD
Floating Point
SIMD
…
Data cache
Constant cache
Shared Memory
Scoreboard & Registerfile
Texture
cache
Special Fcn
SIMD
Thread Block Dispatcher
Block 0
Block K-1
…
Notes: -Thread block -> group of loop iterations (1 to 1024 loop iterations) executed in lock-step on SIMD

## Slide 5: Software Interface
OpenACC
  Higher Productivity
int main(){
...
#pragma acc kernels copyin(a[0:LEN]) copyout(b[0:LEN])
#pragma acc loop independent
for(i=0; i<LEN; ++i) {
b[i] = a[i]+10;
}
...
}
CUDA
  Higher Performance
__global__ void matrixMul(int *a, int *b, int len){
int i=threadIdx.x+blockIdx.x*blockDim.x;
b[i] = a[i]+10;
}
int main(){
...
bytes=LEN*sizeof(int);
cudaMalloc(&a_d, bytes);
cudaMalloc(&b_d, bytes);
cudaMemcpy(a_d, a, bytes, cudaMemcpyHostToDevice);
dim3 gridSize(LEN/16,LEN/16);
dim3 blockSize(16,16);
matrixMul<<<gridSize,blockSize>>>(a_d,b_d,LEN);
cudaMemcpy(c, b_d, bytes, cudaMemcpyDeviceToHost);
...
}
Notes: -Not going to the detail of the code, just showing the relative code size
-Each loop iteration is executed by one thread

## Slide 6: Software-managed Cache In GPUs
OpenACC
...
#pragma acc cache(a[i:256])
{
sum += a[i] + ... + a[i+255];
}
...
CUDA
__shared__ float smc[256];
smc[threadIdx.x] = a[i];
...
float sum = a[i] + ... + a[i+255];
...
GPU Core #1
L1$
Ready Thread Blocks
LDST units & SIMDs
Shared Memory
(SMC)
Scoreboard & Regfile
Other caches
Notes: -Private per core space
-Trivial to use in OpenACC
-In CUDA though, two memory spaces should be maintained
-Data in shared memory is private and not backedup elsewhere

## Slide 7: This Dissertation
Performance
Productivity
Compare high-level & low-level
programming models
IPMACC OpenACC Compiler
(microbenchmarking to tune the compiler)
Major performance bottleneck in
high-level accelerator programming: SMC
OpenACC
CUDA
Implementing cache directive
Enhancing cache Directive
TELEPORT
Proposed
Solutions
Criteria
Approach
Infrastructure
Observation
Chapter 3
Chapter 4
Chapter 5
Chapter 6
Chapter 7

## Slide 8: Outline
Overview
Chapter 3: IPMACC
Chapter 4: Microbenchmarking GPGPUs
Chapter 5: Implementing OpenACC cache Directive
Chapter 6: Enhancing cache Directive
Chapter 7: TELEPORT
Conclusion

## Slide 9: Chapter 3: IPMACC
Developed from scratch to run OpenACC codes on vector processors (GPUs and CPUs):
System Compilers
Translator
to CUDA
to ISPC
to OpenCL
OpenACC API
Hand Optimization
OpenACC Source
Translated
Source
Machine Binary
gcc/nvcc
gcc/ispc
gcc
libopenacc.so
IPMACC

## Slide 10: Chapter 3: IPMACC (2)
Simple usage:
  $ ipmacc sourceacc.c -o gpubinary
  This generates an intermediate CUDA source code
Features:
  Supported directives: data, kernels, loop, cache
  Supported backends: CUDA, OpenCL, and ISPC
  Supports user-defined datatypes and routines
Available to public since Dec 6, 2014:
  https://github.com/lashgar/ipmacc
  Repository includes our benchmarks too

## Slide 11: Chapter 3: IPMACC (2)
Investigating performance gap between CUDA and OpenACC

## Slide 12: Chapter 4: Micro-benchmarking GPGPUs
Micro-benchmarking:
  Understanding micro-architecture through software stress-tests
Purpose:
  To tune IPMACC compiler for best performance
Targets:
  L1 cache memory request handling resources
  Shared memory organization
Available to public since Jun 9, 2015:
  https://github.com/lashgar/microbenchmark

## Slide 13: Chapter 4: Micro-benchmarking GPGPUs (2)
Findings on Tesla C2070 L1 cache: MSHR
  128 MSHR entry, utmost, 8 mergers per entry, at least
  MLP per SM:
    Coalesced = 1024 (128 x 8) & Un-coalesced = 128
Findings on Tesla K20c L1 cache: PRT
  44 PRT entries, utmost, 32 requests per entry (warp size)
  MLP per SM:
    Coalesced/Un-coalesced = 1408 (44 x 32)

## Slide 14: Chapter 4: Micro-benchmarking GPGPUs (3)
Findings on shared memory
  The layout of 2D arrays allocated in the shared memory is found to be the same as flattened 2D arrays
  Adding a small padding in allocation vastly resolves bank conflict

## Slide 15: This Dissertation
Performance
Productivity
Compare high-level & low-level
programming models
IPMACC OpenACC Compiler
(microbenchmarking to tune the compiler)
Major performance bottleneck in
high-level accelerator programming: SMC
OpenACC
CUDA
Implementing cache directive
Enhancing cache Directive
TELEPORT
Proposed
Solutions
Criteria
Approach
Infrastructure
Observation
Chapter 5

## Slide 16: Chapter 5: Implementing cache Directive
First work investigating cache directive implementation
Example:
#pragma acc kernels loop
for(i=1; i<LEN-1; ++i){
int lower = i-1, upper = i+1;
float sum = 0;
#pragma acc cache(a[(i-1):3])
{
for(j=lower; j<=upper; ++j)
sum += a[j];
}
b[i] = sum/(upper-lower+1);
}
GPU Core #1
L1$
Ready Thread Blocks
LDST units & SIMDs
Shared Memory
(SMC)
Scoreboard & Regfile
Other caches

## Slide 17: Chapter 5: Implementing cache Directive (2)
Directive is general, but implementation is hardware specific
  We target NVIDIA GPUs
Critical optimizations:
  Cache sharing, fetch, write policy, index mapping, occupancy
Proposed three implementations
Our best implementation performs near to CUDA, while reducing development effort by 29%
  Evaluated various configurations under 3 test cases, 2 GPUs

## Slide 18: This Dissertation
Performance
Productivity
Compare high-level & low-level
programming models
IPMACC OpenACC Compiler
(microbenchmarking to tune the compiler)
Major performance bottleneck in
high-level accelerator programming: SMC
OpenACC
CUDA
Implementing cache directive
Enhancing cache Directive
TELEPORT
Proposed
Solutions
Criteria
Approach
Infrastructure
Observation
Chapter 6

## Slide 19: Chapter 6: Enhancing cache Directive
cache directive limitation:
Iteration
#1
SMC
...
Iteration
#2
SMC
...
Iteration
#N
SMC
...
...
Read
Private
Read-only
Read
Read
Private
Read-Write
Shared
Read-Only
Shared
Read-Write
Write
Write
Write
Read
Read
Read
Write
Write
Write

## Slide 20: Chapter 6: Enhancing cache Directive (2)
Shared Read-Write SMC is very common in CUDA applications:
  E.g. Reduction, Pathfinder, Hotspot, Dyadic Convolution
We proposed fcw directive to address this limitation
  Shared Read-Write SMC in OpenACC
  Notation is similar to cache directive
  Introduces an inter-iteration communication model for sharing intermediate results
Evaluated under six test-cases:
  Runtime improvement over baseline OpenACC, at a lower development effort than CUDA

## Slide 21: This Dissertation
Performance
Productivity
Compare high-level & low-level
programming models
IPMACC OpenACC Compiler
(microbenchmarking to tune the compiler)
Major performance bottleneck in
high-level accelerator programming: SMC
OpenACC
CUDA
Implementing cache directive
Enhancing cache Directive
TELEPORT
Proposed
Solutions
Criteria
Approach
Infrastructure
Observation
Chapter 7

## Slide 22: Chapter 7: TELEPORT
Key Idea:
  Identify data with sharing opportunities in CUDA kernels
  Fetch the data “automatically” to shared memory
Advantages:
  No extra development effort
  No extra instruction

## Slide 23: Chapter 7: TELEPORT (2)
tid
i
id
blockDim, threadIdx,
blockIdx,
Depends on an induction var
Data dependent
Kernel<<< NTB, blockDim >>> ( <args> );
Constant
Min = 0
Max = blockDim
Known at runtime
tid range is a function
of blockIdx
Notes: Only memory reads are candidates
Range of tid is known if blockIdx is known.

## Slide 24: Chapter 7: TELEPORT (2)
tid
blockDim, threadIdx,
blockIdx,
Kernel<<< NTB, blockDim >>> ( <args> );
cudaSetCTATracker( cost, <tid range>);
cudaSetCTATracker( nodes, <tid range>);
Notes: Only memory reads are candidates
Range of tid is known if blockIdx is known.

## Slide 25: Chapter 7: TELEPORT (2)
Cache
Tag
cudaSetCTATracker( cost, <tid range>);
cudaSetCTATracker( nodes, <tid range>);
GPU
SM2
MC1
MCN
$
L2$
L2$
Interconnect
…
Thread Block Dispatcher
Block NTB-1
…
SM1
Ready Threads
Load/Store Unit
Execution Engine
Other caches
Shared Memory
Scoreboard
On-Hold Thread
Preloader
SM1
$
Block 1
Kernel<<< NTB, blockDim >>> ( <args> );
Block 0
Notes: Only memory reads are candidates
Range of tid is known if blockIdx is known.

## Slide 26: Chapter 7: TELEPORT (3)
Used GPGPU-sim 3.2.2 for modeling TELEPORT
Analyzed 16 benchmarks:
  Limited evaluations to 5 test-cases
Three methods are compared:
  Baseline no-SMC CUDA
  Baseline no-SMC CUDA + TELEPORT
  Hand-optimized CUDA
Evaluations show advantages in:
  Development effort, runtime, dynamic instructions, DRAM accesses, DRAM row locality
Notes: -
-Not replaces all functionalities of CUDA shared memory notation

## Slide 27: Conclusion
Developed & introduced IPMACC OpenACC compiler
Derived set of micro-benchmarkings to understand GPUs
First work investigating cache directive implementation aspect
Proposed a directive to address cache directive limitations
Proposed a hardware/software alternative to CUDA shared memory programming

## Slide 28: List of Publications
Efficient Implementation of OpenACC cache Directive on NVIDIA GPUs Ahmad Lashgar and Amirali Baniasadi To appear in the International Journal of High Performance Computing and Networking (IJHPCN), Special Issue on High-level Programming Approaches for Accelerators
OpenACC cache Directive: Opportunities and Optimizations Ahmad Lashgar and Amirali Baniasadi In proceedings of WACCPD 2016, (in conjunction with SC 2016), Salt Lake City, Utah, USA, November 14, 2016.
Employing Compression Solutions under OpenACC Ebad Salehi, Ahmad Lashgar, and Amirali Baniasadi In proceedings of HIPC 2016, (in conjunction with IPDPS 2016), Chicago, Illinois, USA, May 23-27, 2016.
A Case Study in Reverse Engineering GPGPUs: Outstanding Memory Handling Resources Ahmad Lashgar, Ebad Salehi, and Amirali Baniasadi ACM SIGARCH Computer Architecture News - HEART '15, Volume 43 Issue 4
Employing Software-Managed Caches in OpenACC: Opportunities and Benefits Ahmad Lashgar and Amirali Baniasadi ACM Transactions on Modeling and Performance Evaluation of Computing Systems (ACM ToMPECS), Volume 1 Issue 1, March 2016
Rethinking Prefetching in GPGPUs: Exploiting Unique Opportunities Ahmad Lashgar and Amirali Baniasadi In proceedings of HPCC’17, New York, NY, USA, August 24-26, 2015.
Understanding Outstanding Memory Request Handling Resources in GPGPUs Ahmad Lashgar, Ebad Salehi, and Amirali Baniasadi In proceedings of HEART’6 [Best Paper Candidate], Boston MA, USA, June 1-2, 2015.
IPMACC: Translating OpenACC API to OpenCL Ahmad Lashgar, Alireza Majidi, and Amirali Baniasadi In poster session of the 3rd International Workshop on OpenCL (IWOCL) Stanford University, California, USA, May 11-13, 2015.
A Case Against Small Data Types on GPGPUs Ahmad Lashgar and Amirali Baniasadi In proceedings of IEEE ASAP’25, IBM Research, Zurich, Switzerland, June 18-20, 2014.

## Slide 29
Thank You!
Questions?